## Slide 1
Underwater Diving Operations
Scuba Systems, Surface Supplied Diving (SSD), Hyperbaric Physics, Diving Medical, Communications & Marine Navigation

## Slide 2
1. Technical & Equipment
Mastering Open-Circuit Scuba apparatus, Surface Supplied Diving (SSD) umbilical helmets, air banks, and emergency gas supplies.
Understanding hyperbaric physical gas laws (Boyle, Dalton, Henry, Gay-Lussac) and underwater pressure dynamics.
2. Safety & Field Execution
Diving medical protocols, barotrauma prevention, decompression illness management, and hyperbaric chamber operations.
Standardized underwater communication (hand/rope signals), COLREG marine navigation rules, and in-water rescue circuits.
OPERATIONAL DOMAINS

## Slide 3
Diving Equipment & Systems
Section 01: Scuba Hardware & Surface Supplied Diving (SSD) Infrastructure

## Slide 4
Primary Scuba Hardware
Cylinder: High-pressure aluminum/steel tank (200-300 bar working pressure).
First Stage Regulator: Reduces high cylinder pressure to an intermediate pressure (~9-10 bar above ambient).
Second Stage Regulator: Delivers breathable air at ambient pressure on inhalation demand.
Buoyancy & Monitoring
BCD System: Harness with inflatable bladder, low-pressure inflator, and over-pressure relief valves.
Alternate Air Source: Secondary second-stage (Octopus) for buddy air sharing emergencies.
SPG Gauge: Submersible pressure gauge tracking real-time breathing gas reserves.
SCUBA LIFE SUPPORT SYSTEMS

## Slide 5
SURFACE SUPPLIED DIVING (SSD)
Surface Air Infrastructure
SSD supplies breathable gas from a surface air compressor or high-pressure gas storage rack via a heavy-duty umbilical hose.
Umbilical Bundle: Consists of an air supply hose, pneumofathometer depth line, communications wire, and strength member.
Headgear: Heavy-duty helmets (e.g., Kirby Morgan KM-37) or bandmasks featuring non-return valves and integrated communications.

## Slide 6
Operational Feature | Scuba Diving System | Surface Supplied Diving (SSD)
Gas Supply Limit | Restricted to cylinder volume (e.g., 12L @ 200 bar) | Unlimited surface air supply bank / compressor
Communications | Limited to visual hand signals / slate notes | Continuous hardwire voice communications
Safety Reserve | Onboard bailout / buddy octopus system | Emergency Gas Supply (EGS) bailout cylinder
Diver Mobility | High 3D maneuverability & untethered freedom | Restricted by umbilical length & tether drag
SCUBA VS SSD COMPARISON

## Slide 7
EGS Bailout System
Harness-mounted high pressure cylinder with emergency first stage connected directly to the helmet selector block for instantaneous switchover.
Pneumofathometer
Surface depth-gauge system that reads pressure reflected back from the diver's open-ended hose, providing exact surface depth tracking.
Air Control Panel
Surface manifold managed by the dive tender to monitor manifold pressures, depth gauges, and full-duplex communications.
SPECIALISED SSD COMPONENTS

## Slide 8
Diving Physics & Gas Laws
Section 02: Hydrostatic Pressure, Gas Compression & Dissolution Mechanics

## Slide 9
+1.0 atm
Per 10m (33ft) Seawater Depth
Total Ambient Pressure Calculation
Hydrostatic pressure increases linearly with depth due to the weight of seawater. Total ambient pressure ($P_{\text{total}}$) equals atmospheric pressure plus hydrostatic pressure.
At 20 meters depth: Ambient Pressure = 1.0 atm + 2.0 atm = 3.0 ata total pressure.
HYDROSTATIC PRESSURE MECHANICS

## Slide 10
Pressure-Volume Relationship
At constant temperature, gas volume is inversely proportional to absolute pressure:
Operational Impact: As depth increases, gas volume shrinks and air density increases proportionally. At 3.0 ata (20m), gas volume is 1/3, consuming cylinder gas 3 times faster than at the surface!
BOYLE'S LAW & PRESSURE VOLUME

## Slide 11
Sum of Partial Pressures: The total pressure exerted by a gas mixture is the sum of partial pressures of individual component gases.
Oxygen Toxicity Limit: Air contains 21% Oxygen ($O_2$). Maximum working limit $ppO_2 = 1.4\text{ ata}$ is reached at 56 meters on standard air.
Nitrogen Narcosis Risk: High $ppN_2$ at depths beyond 30m exerts an intoxicating anesthetic effect on the central nervous system.
DALTON'S LAW OF PARTIAL PRESSURES

## Slide 12
Gas Solubility Mechanics
The amount of gas dissolved in a liquid is directly proportional to the partial pressure of that gas above the liquid.
During descent, elevated partial pressure forces inert Nitrogen gas to dissolve into body tissues.
On-Gassing & Off-Gassing
Bottom Time: Tissues absorb Nitrogen until saturation is reached at ambient pressure.
Ascent Elimination: Controlled ascent rates allow Nitrogen to diffuse back into the bloodstream and be safely exhaled through the lungs.
Safety Stop: A 3-minute stop at 5m mitigates micro-bubble formation.
HENRY'S LAW & GAS DISSOLUTION

## Slide 13
Temperature & Pressure Direct Ratio: At constant volume, pressure varies directly with absolute temperature.
Fast Cylinder Filling Heat: Rapidly filling diving cylinders increases internal gas temperature, showing artificially high pressures.
In-Water Cooling Drop: When a hot cylinder is submerged in cold ocean water, temperature drops, causing working pressure to drop proportionally.
CHARLES'S & GAY-LUSSAC'S LAWS

## Slide 14
Diving Physiology & Medical
Section 03: Barotrauma, Decompression Sickness & Hyperbaric Emergency Care

## Slide 15
Middle Ear Squeeze
Failure to equalize Eustachian tubes during descent causes pressure differential across the eardrum, risking tympanic membrane rupture.
Sinus & Mask Squeeze
Failure to exhale into the mask mask space or blocked sinus passages creates negative pressure, causing facial tissue capillary damage.
Pulmonary Over-Expansion
Holding breath during ascent causes expanding lung air to rupture alveoli, resulting in pneumothorax or Arterial Gas Embolism (AGE).
TYPES OF BAROTRAUMA

## Slide 16
Mechanism & Pathology
If ascent is too rapid, Nitrogen comes out of physical solution faster than it can be exhaled, forming inert gas micro-bubbles in blood vessels and joint tissues.
Type I DCS: Joint pain ("The Bends"), localized skin itching, lymphatic swelling.
Type II DCS & Manifestation
Type II DCS (Severe): Neurological numbness, paralysis, respiratory distress ("chokes"), circulatory shock, or inner ear vertigo.
Mitigation: Strict adherence to dive computer NDL limits, ascent rates under 9-18m/min, and mandatory safety stops.
DECOMPRESSION SICKNESS (DCS)

## Slide 17
HYPERBARIC MEDICAL TREATMENT
Emergency Action Protocols
First Aid: Administer 100% surface oxygen immediately via non-rebreather mask to establish an oxygen gradient and accelerate Nitrogen off-gassing.
Hydration & Lay Flat: Keep casualty supine, administer oral/IV fluids, and keep warm.
Recompression Chamber: Definitively treated in a multiplace recompression chamber using US Navy Treatment Tables (e.g., Table 6) to mechanically crush bubbles.

## Slide 18
Nitrogen Narcosis ("Martini Effect")
High inert gas partial pressure causes a narcotic, intoxicating effect on central nervous system lipid membranes at depths exceeding 30m.
Symptoms: Impaired judgment, loss of dexterity, delayed reaction time, euphoria, or sudden anxiety.
Oxygen Toxicity (CNS)
Occurs when breathing high partial pressures of Oxygen ($ppO_2 \ge 1.4\text{ ata}$).
VENTID Symptoms: Visual disturbances, Ear ringing, Nausea, Twitching/Tremors, Irritability, Dizziness, followed by violent grand mal convulsions.
NITROGEN NARCOSIS & O2 TOXICITY

## Slide 19
Diving Signals & Communication
Section 04: Hand Signals, Commercial Line Pulls & Electronic Comms

## Slide 20
Directional Signals
Ascend / Surface: Thumb pointing upward. Descend: Thumb pointing downward. Level Off: Flat hand wave horizontally.
Status & Safety
OK: Circle formed by thumb & index finger. Problem: Hand tilted side-to-side. Equalize: Pointing finger to ear.
Emergency Signals
Out of Air: Slash motion across throat. Share Air: Pointing fingers to mouth. Hold / Stop: Raised flat palm outward.
STANDARD HAND SIGNALS

## Slide 21
Pull Signal | Tender to Diver (Surface Signal) | Diver to Tender (Submerged Signal)
1 Pull | Are you OK? / Confirm status | I am OK / Arrived at bottom
2 Pulls | Pay out more umbilical line | Give me more umbilical line / slack
3 Pulls | Take up slack / stand by | Take up umbilical line slack
4 Pulls | Come up immediately / emergency | Haul me up immediately / Emergency!
COMMERCIAL ROPE PULL SIGNALS

## Slide 22
SSD Hardwire Communications
Utilizes copper communication wires molded into the diver's umbilical bundle attached to helmet microphone and ear speakers.
Full-Duplex Mode: Allows simultaneous open-mic voice communication between diver, surface tender, and supervisor.
Wireless Acoustic Transceivers
Used in technical scuba and search/rescue missions without umbilical lines.
Ultrasonic Carrier Waves: Transmits voice signals through water using high-frequency ultrasonic transducers fitted to full-face masks.
ELECTRONIC & ACOUSTIC COMMS

## Slide 23
Marine Rules & COLREGS
Section 05: International Maritime Organization Flag Rules & Vessel Signals

## Slide 24
DIVER DOWN FLAG REGULATIONS
Maritime Collision Regulations
Alpha Flag (International Code): Rigid blue and white swallow-tailed flag indicating "I have a diver down; keep well clear at slow speed."
Red & White Flag: Recognized in civilian waters (red with diagonal white stripe).
Clearance Standard: Vessels must maintain at least 50m to 100m distance from displayed dive flags.

## Slide 25
Restricted Maneuverability (COLREG Rule 27): Dive vessels engaged in commercial operations display day shapes and lights to warn passing marine traffic.
Day Shapes Display: Three vertical shapes displayed in a line: Ball - Diamond - Ball (Restricted Maneuverability).
Night Lights Display: Vertical light array: Red (Top) - White (Middle) - Red (Bottom) masthead lights.
Safe Side Clearance: Green lights/diamonds indicate the clear side to pass; Red lights/balls indicate the obstructed side where umbilical/diver is located.
DIVE SUPPORT VESSEL NAVIGATION

## Slide 26
Navigation & Rescue Protocols
Section 06: Compass Navigation, Natural Orientation & In-Water Rescue

## Slide 27
UNDERWATER COMPASS NAVIGATION
Compass Alignment Procedure
Lubber Line: Align the center red lubber line directly with the diver's body center line and direction of travel.
Bezel Setting: Rotate the rotating bezel index marks over the north-seeking magnetic needle.
Reciprocal Course: For a 180-degree return path, turn until the needle points to the opposite index mark, keeping body level and kick cycles measured.

## Slide 28
Sand Ripple Patterns
Wave action creates sand wave ripples parallel to the shoreline, offering a reliable grid axis for orienting relative to coastlines.
Sunlight & Rays
Observing ambient sunlight angle and shadow directions provides a quick directional baseline during daytime shallow water dives.
Depth Contours
Following natural seabed slope profiles, reef walls, and current directions ensures accurate return course orientation.
NATURAL NAVIGATION FACTORS

## Slide 29
EMERGENCY ACTION & RESCUE
In-Water Rescue Protocol
Pre-Dive Checks (BWRAF): BCD, Weights, Releases, Air, Final OK.
Controlled Ascent: Secure unresponsive diver from behind, maintain head tilt for airway, vent BCDs (<18m/min rate).
Surface Positivity: Inflate BCDs, ditch ballast weights, establish airway, deliver 1 rescue breath every 5 seconds while towing to exit.

## Slide 30
Questions & Summary
Comprehensive Submerged Operations Training Complete

## Slide 31
https://img1.wsimg.com/isteam/ip/d726989b-0d1b-439a-807a-6dfc5d6436b4/blob-a007ede.png/:/cr=t:0%25,l:0%25,w:100%25,h:100%25/rs=w:400,cg:true
Source: mecdco.com
https://www.mikesdivestore.com/cdn/shop/files/SeacModularPackage.jpg?v=1774608034&width=1214
Source: www.mikesdivestore.com
https://o2bonaire.com/wp-content/uploads/2019/06/Recompression-chamber-Bonaire-28.jpg
Source: o2bonaire.com
https://driveaboatusa.com/wp-content/uploads/2024/08/types_of_diver_down_flags-1.webp
Source: driveaboatusa.com
https://i.ytimg.com/vi/pDE-ilJk0tw/maxresdefault.jpg
Source: www.youtube.com
https://storage1.snappages.site/eupr0m0685/assets/images/6275246_1200x800_500.jpg
Source: www.dansa.org
IMAGE SOURCES